G7
G6
G5
G4
G3
G2
G1
G0
R7
R6
R5
R4
R3
R2
R1
R0
B7
B6
B5
B4
B3
B2
B1
B0

1
0

V

t

Application representation
Desired WS2812B representation

V

t

SPI representation

1
1
1
0
0
0

WS2812B Logic 1:
A high pulse of 0.8us +/-150ns
A low pulse of 0.4us +/-150ns
Total width : 1.25us +/-600ns

WS2812B Logic 0:
A high pulse of 0.4us +/-150ns
A low pulse of 0.8us +/-150ns
Total width : 1.25us +/-600ns

If the SPI bus is run at 3MHz, one SPI bit lasts 0.333us, two SPI bits take 0.667us. These times are within the WS2812B specification for narrow and wide pulse widths. A colour bit value of '1' in the application layer is mapped to an SPI bit pattern of '110'; while a colour bit value of '0' in the application layer is mapped to an SPI bit pattern of '100'. Each application colour byte therefore maps to 3 SPI bytes. A 3 byte Green-Red-Blue colour value in the application layer is converted to a 9 byte SPI sequence and output to the WS2812B.